## Slide 1: Chapter 4
The Processor-II
Reference: Section 4.4, Appendix B, Appendix D

## Slide 2: Datapath With Control
For load instruction these lines hold write register #
For add instruction these lines hold write register #

## Slide 3: The Main Control Unit
Control signals derived from instruction
0
rs
rt
rd
shamt
funct
31:26
5:0
25:21
20:16
15:11
10:6
35 or 43
rs
rt
address
31:26
25:21
20:16
15:0
4
rs
rt
address
31:26
25:21
20:16
15:0
R-type
Load/ Store
Branch
opcode
always read
read, except for load
write for R-type and load
sign-extend and add

## Slide 6
Input
Output
Truth Table Layout

## Slide 11: ALU Control
ALU used for
  Load/Store: F = add
  Branch: F = subtract
  R-type: F depends on funct field
§4.4 A Simple Implementation Scheme
ALU control | Function
0000 | AND
0001 | OR
0010 | add
0110 | subtract
0111 | set-on-less-than
1100 | NOR

## Slide 12: ALU Control
Assume 2-bit ALUOp derived from opcode
  Combinational logic derives ALU control
opcode | ALUOp | Operation | funct | ALU function | ALU control
lw | 00 | load word | XXXXXX | add | 0010
sw | 00 | store word | XXXXXX | add | 0010
beq | 01 | branch equal | XXXXXX | subtract | 0110
R-type | 10 | add | 100000 | add | 0010
 |  | subtract | 100010 | subtract | 0110
 |  | AND | 100100 | AND | 0000
 |  | OR | 100101 | OR | 0001
 |  | set-on-less-than | 101010 | set-on-less-than | 0111

## Slide 13
Row 1
Row 2
Row 7
Input
Output
ALUOp1 = 1 and ALUOp0=1 combination is never
generated, so it is OK to put don’t care for ALUOp1
ALUOp1 = 1 and ALUOp0=1 combination is never
generated, so it is OK to put don’t care for ALUOp0

## Slide 14
Input
Output
Truth Table
Layout

## Slide 15
Operation 2
Don’t care entries help us to have a compact truth table and also optimize the
logic design

## Slide 16
A truth table with don’t care entries in a row minimizes to a function where the input corresponding to don’t care is ignored, for example:
=
=
Optimization using don’t care entries

## Slide 17
Operation 2
Use sum of product term:
. . . . . .
. .

## Slide 18: Datapath With Control

## Slide 19: R-Type Instruction
add $t1, $t2, $t3
sub $t1, $t2, $t3

## Slide 20: Load Instruction
lw $t1, 100($t2)
What about addi ?

## Slide 21: Branch-on-Equal Instruction

## Slide 22: Implementing Jumps
Jump uses word address
Update PC with concatenation of
  Top 4 bits of old PC
  26-bit jump address
Need an extra control signal decoded from opcode
2
address
31:26
25:0
Jump

## Slide 23: Implementing Jumps

## Slide 24: Datapath With Jumps Added