## Slide 1: Chapter 5
Large and Fast: Exploiting Memory Hierarchy

## Slide 2: Principle of Locality
Programs access a small proportion of their address space at any time
Temporal locality
  Items accessed recently are likely to be accessed again soon
  e.g., instructions in a loop, induction variables
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  E.g., sequential instruction access, array data
§5.1 Introduction

## Slide 3: Taking Advantage of Locality
Memory hierarchy
Store everything on disk
Copy recently accessed (and nearby) items from disk to smaller DRAM memory
  Main memory
Copy more recently accessed (and nearby) items from DRAM to smaller SRAM memory
  Cache memory attached to CPU

## Slide 4: Taking Advantage of Locality
a block of 4 words
cache that can accommodate a max of 2 blocks at a time
CPU
cpu needs word#2 of a block

## Slide 5: Taking Advantage of Locality
a block of 4 words
cache that can accommodate a max of 2 blocks at a time
CPU

## Slide 6: Temporal Locality
a block of 4 words
cache that can accommodate a max of 2 blocks at a time
CPU
cpu repeatedly access word#2 of the block

## Slide 7: Spatial Locality
a block of 4 words
cache that can accommodate a max of 2 blocks at a time
CPU
cpu next time access word#1 of the block

## Slide 8: Memory Hierarchy Levels
Block (aka line): unit of copying
  May be multiple words
If accessed data is present in upper level
  Hit: access satisfied by upper level
    Hit ratio: hits/accesses
If accessed data is absent
  Miss: block copied from lower level
    Time taken: miss penalty
    Miss ratio: misses/accesses = 1 – hit ratio
  Then accessed data supplied from upper level

## Slide 9: Memory Technology
Static RAM (SRAM)
  0.5ns – 2.5ns, $2000 – $5000 per GB
Dynamic RAM (DRAM)
  50ns – 70ns, $20 – $75 per GB
Magnetic disk
  5ms – 20ms, $0.20 – $2 per GB
Ideal memory
  Access time of SRAM
  Capacity and cost/GB of disk
§5.2 Memory Technologies

## Slide 10: Memory Addressing Basics
Byte Addressable
Accessing words and word addresses
Accessing blocks and block addresses
§5.2 Memory Technologies

## Slide 11: Byte, Word, Block Addresses
Example:
Total memory 256 bytes
1 Word = 4 bytes, 1 Block = 8 Words
Byte Addressable ?
Word Addressable ?
Block Addressable?
§5.2 Memory Technologies

## Slide 12: Byte, Word, Block Addresses
§5.2 Memory Technologies
Byte
Word
Block
1 Word = 4 bytes
1 Block = 8 Words

## Slide 13: Byte, Word, Block Addresses
§5.2 Memory Technologies
Byte
word #0
word #1
word #63
1 Word = 4 bytes

## Slide 14: Byte, Word, Block Addresses
§5.2 Memory Technologies
Byte
block #0
block #1
block #7
1 Block = 8 Words

## Slide 15: Cache Memory
Cache memory
  The level of the memory hierarchy closest to the CPU
Given accesses X1, …, Xn–1, Xn
§5.3 The Basics of Caches
How do we know if the data is present?
Where do we look?

## Slide 16: Associative Caches
Fully associative
  Allow a given block to go in any cache entry
block #0
block #1
block #7
Example: Consider a cache of 4 blocks. What happens if CPU accesses
memory address 32 ?
Initially cache is empty. Access to 32 is a miss!
001
block #1 (M[32:63])
Data
Tag
Notes: 4 blocks = 4 rows -> assuming 8 words per block = 32 bit block size, block #0 = (M[0:31]), block #1 = (M[32:63]), etc. etc. NOTE: Because block size is 32-bits, we know that the index/offset is log(2^5 = 32) = 5

## Slide 17: Associative Caches
Fully associative
  What happens now if CPU accesses memory address 38 ( 0 0 1 0 0 1 1 0 )? block #1 contains M[38] and is already in the cache, so it is a hit !
  How do we know it is in cache?
  Search all tag entries and look for a match
block #0
block #1
block #7
001
M[32:63]
Data
Tag

## Slide 18: Associative Caches
Fully associative
  What happens now if CPU accesses memory address 1 ( 0 0 0 0 0 0 0 1)? block #0 contains M[1] and is not in the cache, so it is a miss !
  How do we know it is not in cache?
  Search all tag entries and found no match
block #0
block #1
block #7
001
M[32:63]
Data
Tag
000
M[0:31]

## Slide 19: Associative Caches
Fully associative
  What happens now if CPU accesses memory address 9 ( 0 0 0 0 1 0 0 1)? block #0 contains M[9] and is in the cache, so it is a hit !
block #0
block #1
block #7
001
M[32:63]
Data
Tag
000
M[0:31]

## Slide 20: Associative Caches
Fully associative
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once
  Comparator per entry (expensive)

## Slide 21: Direct Mapped Caches
Direct Mapped
  Allow a given memory block to go to only specific cache entry determined by the memory block address
block #0
Data
Tag
block #1
block #2
block #3
block #4
block #5
block #6
block #7

## Slide 22: Direct Mapped Caches
Direct Mapped
  Allow a given memory block to go to only specific cache entry determined by the memory block address
block #0
Data
Tag
block #1
block #2
block #3
block #4
block #5
block #6
block #7

## Slide 23: Direct Mapped Caches
Direct Mapped
  Allow a given memory block to go to only specific cache entry determined by the memory block address
block #0
Data
Tag
block #1
block #2
block #3
block #4
block #5
block #6
block #7

## Slide 24: Direct Mapped Caches
Direct Mapped
  Allow a given memory block to go to only specific cache entry determined by the memory block address
block #0
Data
Tag
block #1
block #2
block #3
block #4
block #5
block #6
block #7

## Slide 25: Direct Mapped Caches
Direct Mapped
  Allow a given memory block to go to only specific cache entry determined by the memory block address
block #0
Data
Tag
block #1
block #2
block #3
block #4
block #5
block #6
block #7

## Slide 26: Direct Mapped Caches
Direct Mapped
  Allow a given memory block to go to only specific cache entry determined by the memory block address
block #0
Data
Tag
block #1
block #2
block #3
block #4
block #5
block #6
block #7

## Slide 27: Direct Mapped Caches
Direct Mapped
  Allow a given memory block to go to only specific cache entry determined by the memory block address
block #0
Data
Tag
block #1
block #2
block #3
block #4
block #5
block #6
block #7
In fully associative a cache block can accommodate any of the eight memory blocks. In case of direct mapped a cache block can accommodate only two ‘specific’ memory blocks (block#0 and block#4)

## Slide 28: Direct Mapped Caches
Direct Mapped
  Allow a given memory block to go to only specific cache entry determined by the memory block address
block #0
Data
Tag
block #1
block #2
block #3
block #4
block #5
block #6
block #7
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx

## Slide 29: Direct Mapped Caches
Direct Mapped
  Which memory block is currently occupying is determined by the tag bit.
block #0
Data
Tag
block #1
block #2
block #3
block #4
block #5
block #6
block #7
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx

## Slide 30: Direct Mapped Caches
Direct Mapped
  Allow a given memory block to go to only specific cache entry determined by the memory block address
block #0
0
Block #0 (M[0:31])
Data
Tag
block #1
block #2
block #3
block #4
block #5
block #6
block #7
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx

## Slide 31: Direct Mapped Caches
Direct Mapped
  Allow a given memory block to go to only specific cache entry determined by the memory block address
block #0
1
Block #4 (M[128:159])
Data
Tag
block #1
block #2
block #3
block #4
block #5
block #6
block #7
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx

## Slide 32: Direct Mapped Caches
Direct Mapped
  How do we know where does a memory block go in the cache (mapping of a memory block to a cache block)
block #0
Data
Tag
block #1
block #2
block #3
block #4
block #5
block #6
block #7
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx

## Slide 33: Direct Mapped Caches
Direct Mapped Example
  Process access memory byte addresses: 28, 62, 118. Assume cache is initially empty.
28: 0 0 0 1 1 1 0 0 block#0
28: 0 0 0 1 1 1 0 0 cache block#0
When processor access 28, it check the tag for
cache block#0 (00). As there is no tag, it considers a miss, and load the block#0 from memory to cache block #0 (00)

## Slide 34: Direct Mapped Caches
Direct Mapped Example
  Process access memory byte addresses: 28, 62, 118. Assume cache is initially empty.
block #0
0
Block#0 (M[0:31])
Data
Tag
block #1
block #2
block #3
block #4
block #5
block #6
block #7
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
28: 0 0 0 1 1 1 0 0 block#0
28: 0 0 0 1 1 1 0 0 cache block#0 (00)
cache block#0
cache block#1
cache block#2
cache block#3

## Slide 35: Direct Mapped Caches
Direct Mapped Example
  Process access memory byte addresses: 28, 62, 118. Assume cache is initially empty.
block #0
0
Block#0 (M[0:31])
Data
Tag
0
Block#1 (M[32:63])
block #1
block #2
block #3
block #4
block #5
block #6
block #7
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
62: 0 0 1 1 1 1 1 0 block#1
62: 0 0 1 1 1 1 1 0 cache block#1 (01)
cache block#0
cache block#1
cache block#2
cache block#3

## Slide 36: Direct Mapped Caches
Direct Mapped Example
  Process access memory byte addresses: 28, 62, 129. Assume cache is initially empty.
block #0
1
Block#4 (M[128:159])
Data
Tag
0
Block#1 (M[32:63])
block #1
block #2
block #3
block #4
block #5
block #6
block #7
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
xxxxx
129: 1 0 0 0 0 0 0 1 block#4
129: 1 0 0 0 0 0 0 1 cache block#0 (00)
cache block#0
cache block#1
cache block#2
cache block#3

## Slide 37: Tags Bits
28: 0 0 0 1 1 1 0 0 cache block#0 (00)
Tag Bit
28: 0 0 0 1 1 1 0 0 cache block#0 (00)
Tag Bits
Direct Mapped
Fully Associative

## Slide 38: Valid Bits
Given an address, we identify the tag bits of the address and check whether these bits exist in the tag field of the cache.
  For fully associative cache, we look at all cache blocks tag fields
  For direct mapped, we only look at a tag field of a specific cache block
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0

## Slide 39: Cache Example
8-blocks, 1 word/block, direct mapped
Initial cache state as shown below
Accesses words (word address): 22, 26, 16, 3, 16
Show the state of cache after each access and whether the access is a hit or a miss
  Use max word address used (26 in our case) to determine the number of bits you will use for the memory byte address. Closest integer to 26 that is power of 2 is 32. This gives 5 bits for the word address and 2 bits for the byte offset within a word for a total of 7-bits memory byte address.
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 

## Slide 40: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Word #22 (Mem[88:91])
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110
1 Word =
4 Bytes

## Slide 41: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Word #26
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Word #22
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010

## Slide 42: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Word #26
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Word #22
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010

## Slide 43: Cache Example
What would have changed if we
had assumed that the memory
address consists of 6 bits and not
5 bits?
Hits and mIsses ratio?
Number of bits in tag?
Both answers are correct!
Can we assume memory address
of 4-bits?

## Slide 44: Address Subdivision
32-bit memory address
Direct mapped 1024 blocks
1 block = 1 Word = 4 bytes

## Slide 45: Example: Larger Block Size
First Approach:
Binary representation of 1200 using 32 bits
0000 0000 0000 0000 0000 0100 1011 0000
Total memory as in the previous example: 2^32 Bytes
Direct mapped cache of 64 blocks, 16 bytes/block. Show the partitioning of memory address: tag, cache block index, and byte offset within a block
Tag
Index
Offset
0
3
4
9
10
31
4 bits
6 bits
22 bits
To what cache block number does memory address 1200 map?
Second Approach:
Memory block address = 1200/16 = 75
Cache block number = 75 modulo 64 = 11
Block number = 11
Notes: YELLOW: Wtf? 2^32 bytes?? Where does this come from?
4 bits of offset because each block has 16 bytes -> log(2^4 = 16) = 4
6 bits of index because there are 64 blocks -> log(2^6 = 64) = 6 Tag is 22 because 32 – 6 – 4 = 22

## Slide 46: Set Associative Caches
Fully associative
  Allows a given memory block to go in any cache entry. Requires all entries to be searched at once
Direct Mapped
  Allows a given memory block to go only a specific cache entry (too restrictive). Requires only one entry to be searched
Set Associative
  Allows a given memory block to go to one-of-two or one-of-four or one-of-n possible cache blocks

## Slide 47: 2-Way Set Associative
Example: Total Memory 256 Bytes; 1 Block = 8 Words, 1 Word = 4 Bytes,
Total number of Cache blocks = 4
block #0
Data
Tag
block #1
block #2
block #3
block #4
block #5
block #6
block #7
Tag
Data
Way 0
Way 1
Set 0
Set 1
Number of sets = # of Cache Blocks / # of ways
= 4/2 = 2
A memory block is direct mapped to a set and
within a set it has an option to go to one of the two
cache blocks (2–way)

## Slide 48: 2-Way Set Associative
Example: Total Memory 256 Bytes; 1 Block = 8 Words, 1 Word = 4 Bytes,
Total number of Cache blocks = 4
block #0
00
Block #0 M[0:31]
Data
Tag
block #1
block #2
block #3
block #4
block #5
block #6
block #7
Tag
Data
Way 0
Way 1
Set 0
Set 1
Number of sets = # of Cache Blocks / # of ways
= 4/2 = 2
A memory block is direct mapped to a set and
within a set it has an option to go to one of the two
cache blocks (2–way)
28: 0 0 0 1 1 1 0 0
Set index (set #0)
Tag Bits

## Slide 49: Spectrum of Associativity
For a cache with 8 cache blocks
Number of sets =
# of Cache Blocks / # of ways

## Slide 50: Associativity Example
Compare 4-block caches in terms of number of hits/misses
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Cache
Block #0
Block #8
Block #6
For computing hit/miss do we need memory size?
  Block access sequence: 0 (miss), 8 (miss), 0 (miss), 6 (miss), 8 (miss)

## Slide 51: Associativity Example
2-Way Set Associative
Block #0
Block #8
Block #6
  Block access sequence: 0 (miss)
block #0
Data
Tag
Tag
Data
Way 0
Way 1
Set 0
Set 1

## Slide 52: Associativity Example
2-Way Set Associative
Block #0
Block #8
Block #6
  Block access sequence: 0 (miss), 8 (miss)
block #0
Data
Tag
block #8
Tag
Data
Way 0
Way 1
Set 0
Set 1

## Slide 53: Associativity Example
2-Way Set Associative
Block #0
Block #8
Block #6
  Block access sequence: 0 (miss), 8 (miss), 0 (hit)
block #0
Data
Tag
block #8
Tag
Data
Way 0
Way 1
Set 0
Set 1

## Slide 54: Associativity Example
2-Way Set Associative
Block #0
Block #8
Block #6
  Block access sequence: 0 (miss), 8 (miss), 0 (hit), 6 (miss)
block #0
Data
Tag
block #6
Tag
Data
Way 0
Way 1
Set 0
Set 1
replaces least recently
used

## Slide 55: Associativity Example
2-Way Set Associative
Block #0
Block #8
Block #6
  Block access sequence: 0 (miss), 8 (miss), 0 (hit), 6 (miss), 8(miss)
block #8
Data
Tag
block #6
Tag
Data
Way 0
Way 1
Set 0
Set 1
replaces least recently
used

## Slide 56: Associativity Example
Fully Associative
Block #0
Cache
Block #8
Block #6
Block #0
Block #8
Block #6
  Block access sequence: 0 (miss), 8 (miss), 0 (hit), 6 (miss), 8 (hit)

## Slide 57: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
Simulation of a system with 64KB D-cache, 16-word blocks, SPEC2000
  1-way: 10.3%
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%

## Slide 58: Set Associative Cache Organization
32-bit memory address
4-Way Associative with a total of 1024 blocks
1 block = 1 Word = 4 bytes

## Slide 59: Replacement Policy
Direct mapped: no choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard beyond that
Random
  Gives approximately the same performance as LRU for high associativity

## Slide 60: Block Size Considerations
Larger blocks should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger blocks  fewer of them
    More competition  increased miss rate
Larger miss penalty
  Can override benefit of reduced miss rate
  Early restart and critical-word-first can help

## Slide 61: Cache Misses
On cache hit, CPU proceeds normally
On cache miss
  Stall the CPU pipeline
  Fetch block from next level of hierarchy
  Instruction cache miss
    Restart instruction fetch
  Data cache miss
    Complete data access

## Slide 62: Write to Memory
Two types of policies exist in current architectures
  Write Through
    What happens in case of a hit?
    What happens in case of a miss?
  Write Back
    What happens in case of a hit?
    What happens in case of a miss?

## Slide 63: Hit : Write-Through
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
Write through: also update memory
But makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full

## Slide 64: Hit: Write-Back
Alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is dirty
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow replacing block to be read first

## Slide 65: Miss
Write-Through
  Allocate on miss: fetch the block
    After the block is fetched and placed into cache , we can overwrite the word that caused the miss into the cache block. We also write the word to the main memory
Write-Back
  Fetch the block