## Slide 1: Chapter 5
Large and Fast: Exploiting Memory Hierarchy

## Slide 2: Measuring Cache Performance
Components of CPU time
  Program execution cycles
    Includes cache hit time
  Memory stall cycles
    Mainly from cache misses
With simplifying assumptions:
§5.4 Measuring and Improving Cache Performance

## Slide 3: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 2
  Load & stores are 36% of instructions
How much faster a processor would run with a perfect cache that never missed?

## Slide 4: Cache Performance Example
CPU time with stalls
  I x CPI_stall x Clock Cycle
CPU time with perfect cache
    I x CPI_perfect x Clock Cycle
How much faster?
  CPU time with stalls/CPU time with perfect cache = CPI_stall/ CPI_perfect

## Slide 5: Cache Performance Example
Miss cycles per instruction
  I-cache: 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
Actual CPI (CPI_stall) = 2 + 2 + 1.44 = 5.44
  Ideal CPU is 5.44/2 =2.72 times faster

## Slide 6: Cache Performance Example
How much faster a processor would run with a perfect cache in the previous example, if we reduce the CPI from 2 to 1 without changing the clock rate?
  CPI_Stall = 1 + 2 + 1.44 = 4.44
  CPI_Ideal (with perfect cache) = 1
  Speed up = 4.44/1 = 4.44
What happens to the amount of time spent on memory stalls in the two cases?
  Fraction of time spent on memory in first case (CPI = 2): 3.44/5.44 = 63%
  Fraction of time spent on memory in first case (CPI = 1): 3.44/4.44 = 77%

## Slide 7: Average Access Time
Hit time is also important for performance
Average memory access time (AMAT)
  AMAT = Hit time + Miss rate × Miss penalty
Example
  CPU with 1ns clock, hit time = 1 cycle, miss penalty = 20 cycles, I-cache miss rate = 5%
  AMAT = 1 + 0.05 × 20 = 2ns
    2 cycles per instruction

## Slide 8: Performance Summary
When CPU performance increased
  Miss penalty becomes more significant
Decreasing base CPI
  Greater proportion of time spent on memory stalls
Increasing clock rate
  Memory stalls account for more CPU cycles
    Miss Cycle Penalty 100 cycles for 1 GHz Clock
    For same memory but increase clock rate to 2 GHz, miss penalty is 200 cycles
Can’t neglect cache behavior when evaluating system performance

## Slide 9: Multilevel Caches
Primary cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Main memory services L-2 cache misses
Some high-end systems include L-3 cache

## Slide 10: Multilevel Cache Example
Given
  CPU base CPI = 1, clock rate = 4GHz
  Miss rate/instruction = 2%
  Main memory access time = 100ns
With just primary cache
  Miss penalty = 100ns/0.25ns = 400 cycles
  Effective CPI = 1 + 0.02 × 400 = 9

## Slide 11: Example (cont.)
Now add L-2 cache
  Access time = 5ns
  Global miss rate to main memory = 0.5%
Primary miss with L-2 hit
  Penalty = 5ns/0.25ns = 20 cycles
Primary miss with L-2 miss
  Extra penalty = 500 cycles
CPI = 1 + 0.02 × 20 + 0.005 × 400 = 3.4
Performance ratio = 9/3.4 = 2.6

## Slide 12: Multilevel Cache Considerations
Primary cache
  Focus on minimal hit time
L-2 cache
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact
Results
  L-1 cache usually smaller than a single cache
  L-1 block size smaller than L-2 block size