## Slide 1
Parallel Processors

## Slide 2: Hardware and Software
Hardware
  Serial: e.g., Pentium 4
  Parallel: e.g., quad-core Xeon e5345
Software
  Sequential: e.g., matrix multiplication
  Concurrent: e.g., operating system
Sequential/concurrent software can run on serial/parallel hardware
  Challenge: making effective use of parallel hardware

## Slide 3: Parallel Programming
Parallel software is the problem
Need to get significant performance improvement
  Otherwise, just use a faster uniprocessor, since it’s easier!
Difficulties
  Partitioning
  Coordination
  Communications overhead
§6.2 The Difficulty of Creating Parallel Processing Programs

## Slide 4: Amdahl’s Law
Sequential part can limit speedup
Example: Execution time for a program: 1s
  All of the program can be parallelized
  With 100 processors, the new execution time is 1/100 s
  Speed up = 1s/0.01s = 100
Example: Execution time for a program: 1s
  Computation corresponding to time 0.9s (out of 1s) an be parallelized, the other computation cannot be parallelized.
  With 100 processors, the new execution time is: 0.9/100s + 0.1s
  Speed up = 1s/(0.9/100s + 0.1s) = 9.2
Example: Execution time for a program: 1s
  Computation corresponding to time 0.9s (out of 1s) an be parallelized, the other computation cannot be parallelized.
  With infinite processors, the new execution time approaches to: 0.1s
  Speed up = 1s/(0.1s) = 10

## Slide 5: Scaling Example
Workload: sum of 10 scalars, and 10 × 10 matrix sum
  Speed up from 10 to 100 processors
Single processor: Time = (10 + 100) × tadd
10 processors
  Time = 10 × tadd + 100/10 × tadd = 20 × tadd
  Speedup = 110/20 = 5.5 (55% of potential)
100 processors
  Time = 10 × tadd + 100/100 × tadd = 11 × tadd
  Speedup = 110/11 = 10 (10% of potential)
Assumes load can be balanced across processors

## Slide 6: Scaling Example
Workload: sum of 10 scalars, and 10 × 10 matrix sum
Single processor: Time = (10 + 100) × tadd
10 processors
  Time = 10 × tadd + 100/10 × tadd = 20 × tadd
  Speedup = 110/20 = 5.5 (55% of potential)

## Slide 7: Scaling Example
Workload: sum of 10 scalars, and 10 × 10 matrix sum
Single processor: Time = (10 + 100) × tadd
100 processors
  Time = 10 × tadd + 100/100 × tadd = 11 × tadd
  Speedup = 110/11 = 10 (10% of potential)

## Slide 8
Load Balancing
Sum of 10 scalars, and 32 × 32 matrix sum on 100 processors
Load Balance: Each processor is adding 10 matrix elements
Speedup = (10+1000)/20 = 50.5
Load Unbalance: One processor adds 20 matrix elements, and the rest 980
additions are distributed uniformly amongst 99 processors
What happens if one processor adds 100 elements?

## Slide 9: Multithreading
Performing multiple threads of execution in parallel
  Replicate registers, PC, etc.
  Fast switching between threads
Fine-grain multithreading
  Switch threads after each cycle
  Interleave instruction execution
  If one thread stalls, others are executed
Coarse-grain multithreading
  Only switch on long stall (e.g., L2-cache miss)
  Simplifies hardware, but doesn’t hide short stalls (eg, data hazards)
§6.4 Hardware Multithreading

## Slide 10: Shared Memory
SMP: shared memory multiprocessor
  Hardware provides single physical address space for all processors
  Synchronize shared variables using locks
  Memory access time
    UMA (uniform) vs. NUMA (nonuniform)
§6.5 Multicore and Other Shared Memory Multiprocessors

## Slide 11: GPU Architectures
Processing is highly data-parallel
  GPUs are highly multithreaded
  Use thread switching to hide memory latency
    Less reliance on multi-level caches
  Graphics memory is wide and high-bandwidth
Trend toward general purpose GPUs
  Heterogeneous CPU/GPU systems
  CPU for sequential code, GPU for parallel code
Programming languages/APIs
  DirectX, OpenGL
  C for Graphics (Cg), High Level Shader Language (HLSL)
  Compute Unified Device Architecture (CUDA)

## Slide 12: Message Passing
Each processor has private physical address space
Hardware sends/receives messages between processors
§6.7 Clusters, WSC, and Other Message-Passing MPs

## Slide 13: Loosely Coupled Clusters
Network of independent computers
  Each has private memory and OS
  Connected using I/O system
    E.g., Ethernet/switch, Internet
Suitable for applications with independent tasks
  Web servers, databases, simulations, …
High availability, scalable, affordable
Problems
  Administration cost (prefer virtual machines)
  Low interconnect bandwidth
    c.f. processor/memory bandwidth on an SMP

## Slide 14: Parallel Benchmarks
Linpack: matrix linear algebra
SPECrate: parallel run of SPEC CPU programs
  Job-level parallelism
SPLASH: Stanford Parallel Applications for Shared Memory
  Mix of kernels and applications, strong scaling
NAS (NASA Advanced Supercomputing) suite
  computational fluid dynamics kernels
PARSEC (Princeton Application Repository for Shared Memory Computers) suite
  Multithreaded applications using Pthreads and OpenMP
§6.10 Multiprocessor Benchmarks and Performance Models

## Slide 15: Modeling Performance
CPU
MEMORY
CPU can operate at
16 GFLOPS/s
Peak Memory Bandwidth
16 GB/s
We have a program that on average perform 1/8 FLOPS per byte access of data
What is the maximum performance I can get for this program? 16 GFLOPS/s ?

## Slide 16: Modeling Performance
We have a program that on average perform 1/8 FLOPS per byte access of data
How much data we can move in 1s to CPU? 16 GB
How many operations CPU can perform in 1s? 16 GB * (1/8 FLOPS/B) = 2 GFLOPS/s

## Slide 17: Modeling Performance
We have a program that on average perform 1/4 FLOPS per byte access of data
How much data we can move in 1s to CPU? 16 GB
How many operations CPU can perform in 1s? 16 GB * (1/4 FLOPS/B) = 4 GFLOPS/s

## Slide 18: Modeling Performance
We have a program that on average perform 1 FLOPS per byte access of data
How much data we can move in 1s to CPU? 16 GB
How many operations CPU can perform in 1s? 16 GB * (1 FLOPS/B) = 16 GFLOPS/s

## Slide 19: Modeling Performance
We have a program that on average perform 2 FLOPS per byte access of data
How much data we can move in 1s to CPU? 16 GB
How many operations CPU can perform in 1s? 16 GB * (2 FLOPS/B) = 32 GFLOPS/s
Is that possible? The maximum CPU can perform is 16 GFLOPS/s
Performance = MIN ( Bandwidth * Arithmetic Intensity, Peak CPU Performance)

## Slide 20: Roofline Diagram
Attainable GPLOPs/sec
= Min ( Peak Memory BW × Arithmetic Intensity, Peak FP Performance )

## Slide 21: Concluding Remarks
Goal: higher performance by using multiple processors
Difficulties
  Developing parallel software
  Devising appropriate architectures
§6.14 Concluding Remarks