## Slide 1: CS 270 – Introduction to Computer Architecture II
§1.1 Introduction

## Slide 2: Course Description
COMPUTER
Processor
Memory
Program /Data
Devices
Control
Datapath
Input
Output
CS 270 is a second course in a two semester sequence; CS 170/270. CS 170 is a prerequisite for CS 270.
Focus: Shaded region in the figure below.

## Slide 3: Course Description
Design and operation of an ALU (Arithmetic/Logic Unit)
Implementation and control of single and multicycle processors
Processor pipelining
Technology and operation of the memory hierarchy (cache-RAM-disk) as well as virtual memory
Importance of performance and the strong connection between the hardware and software

## Slide 4: Text and Topics
Computer Organization and Design, 5th Edition, David A. Patterson and John L. Hennessy
The same text is used in both CS 170 and CS 270. The topics covered in CS 270 are:
  Overview of the Course, Review Chapter 1 and Appendix B
  Processor - Chapter 4, Controller - Appendix D
  Exploiting memory hierarchy - Chapter 5
  Parallel computing overview - Chapter 6

## Slide 5: Grading
Your grade will be based on a total of 100 points with the following distribution.
  Five homework assignments: 15 points
  Quizzes (unannounced, closed book and notes): 15 points
  Two midterms (open book and notes): 30 points
  Final examination (comprehensive, open book and notes): 40 points

## Slide 6: Homework Assignments
Homework assignment will be posted on the website.
A homework assignment will be collected in the class on the due date and graded on a range of 0 to 10.
Solutions for the homework will be posted on the website.

## Slide 7: Quizzes
Several quizzes will be given throughout the course.
The quiz will be given at the beginning of a class and it will take at most 15 minutes to complete the quiz.
The schedule for these quizzes will NOT be posted.
Quizzes will be based on the material covered in the previous lecture. It is advisable that after each lecture you review the covered material so that you are ready for the quiz.
If you miss a quiz, you will be assigned a score of zero for that quiz.
One quiz with the lowest score will be dropped.
There will be no makeup if you miss a quiz. Computer Organization and

## Slide 8: Is Computer Smart?
Hardware only understands electrical signals of the form of high and low voltage (ON/OFF)
  Need to code the instruction in low and high voltage electrical signals
Binary System
  Ideal for representing machine code as it is based on two symbols (1 and 0) that directly map to high and low voltage electrical signals
  For example “10010011” is the machine code for an instruction to add two numbers
§1.2 Below Your Program
Computer Hardware
Electrical signal (ON/OFF)

## Slide 9: More Layers of Software –Look Smarter
High-level language
  Level of abstraction closer to problem domain
  Provides for productivity and portability
Assembly language
  Textual representation of instructions
Hardware representation
  Binary digits (bits)
  Encoded instructions and data

## Slide 10: Below Your Program
Application software
  Written in high-level language
System software
  Compiler: translates HLL code to machine code
  Operating System: service code
    Handling input/output
    Managing memory and storage
    Scheduling tasks & sharing resources
Hardware
  Processor, memory, I/O controllers
§1.2 Below Your Program

## Slide 11: The Computer Revolution
Progress in computer technology
  Underpinned by Moore’s Law
Makes novel applications feasible
  Computers in automobiles
  Cell phones
  Human genome project
  World Wide Web
  Search Engines
Computers are pervasive
§1.1 Introduction

## Slide 12: Uniprocessor Performance
§1.6 The Sea Change: The Switch to Multiprocessors
Constrained by power, instruction-level parallelism, memory latency

## Slide 13: Multiprocessors
Multicore microprocessors
  More than one processor per chip
Requires explicitly parallel programming
  Compare with instruction level parallelism
    Hardware executes multiple instructions at once
    Hidden from the programmer
  Hard to do
    Programming for performance
    Load balancing
    Optimizing communication and synchronization

## Slide 14: Anatomy of Computer
COMPUTER
Processor
Memory
Program /Data
Devices
Control
Datapath
Input
Output

## Slide 15: Inside the Processor (CPU)
Datapath: performs operations on data
Control: sequences datapath, memory, ...
Cache memory
  Small fast SRAM memory for immediate access to data

## Slide 16: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc
The BIG Picture

## Slide 17: Appendix B
Basics of Logic Design

## Slide 18: Logic Design Basics
§4.2 Logic Design Conventions
Objective:
To understand how to build a processor
32
32
32
operation
result
a
b
ALU
Program in C++
Compiler + Assembler

## Slide 19: Logic Design Basics
§4.2 Logic Design Conventions
Information encoded in binary
  Low voltage = 0, High voltage = 1
  One wire per bit
  Multi-bit data encoded on multi-wire buses
Combinational element
  Operate on data
  Output is a function of input
State (sequential) elements
  Store information

## Slide 20: Combinational and Sequential Logic
§4.2 Logic Design Conventions
Combinational logic: A logic system whose blocks do not contain memory and hence compute the same output given the same input.
Sequential logic A group of logic elements that contain memory and hence whose value depends on the inputs as well as the current contents of the memory.

## Slide 21: Combinational Elements
AND-gate
  Y = A & B
A
B
Y
I0
I1
Y
M u x
S
Multiplexer
  Y = S ? I1 : I0
A
B
Y
+
A
B
Y
ALU
F
Adder
  Y = A + B
Arithmetic/Logic Unit
  Y = F(A, B)

## Slide 22: Combinational Elements
Output is completely specified by the input
  TRUTH TABLE is a way of describing how an output of a combinational logic depends on the input – completely specifies the logic function
Example: Basic logic function such as AND
INPUT |  | OUTPUT
A | B | Y
1 | 0 | 0
0 | 1 | 0
0 | 0 | 0
1 | 1 | 1
How many entries in a truth table?

## Slide 23: Truth Table

## Slide 24: Reminder
§4.2 Logic Design Conventions
Please review what I covered in the class today.
Next class could be a quiz!!